## Slide 1: Multi-Switch Cooperative Sketch-based Monitoring
Wei-Te Lu 呂韋德
Advisor：Ching-Ju Lin 林靖茹
Shiao-Li Tsao 曹孝櫟

## Slide 2: Network Measurement
Foundation for network applications
Network Monitoring
Network Security
Analysis
Defense
Network Measurement
Notes: 在一個網路系統當中，網路量測扮演著一個十分重要的腳色。因為對於諸多網路應用以及管理來說，量測是他們不可或缺的基礎，像是網路狀態的監控或者是網路安全的防禦等等，都需要仰賴網路量測的結果，來做出相對應的分析或者是反應。
因此，為了讓這些application可以正常運作，量測的方法是十分重要且不可或缺的

## Slide 3: Existing Measurement Methods
flow
sample
Network Measurement
Sample
Sketch
4+1 | 52 | 31
5 | 20 | 3+1
14 | 2+1 | 9
74+1 | 3 | 6
F1
F2
h1(.)
h2(.)
h3(.)
h4(.)
Hash-based
flow
flow
Notes: 那麼，目前量測的方法 大概可以分成以下兩種
首先 第一種是sample based的方法，在這類方法中，他們會從flow 中sample packet出來累計量測，但是為了維持一定的準確度，往往這類方法都需要相當大的sampling rate ，
而如此一來，會造成諸如cpu 或者是bandwidth等等系統龐大的overhead
而與之相反的另一種方法則是sketch based的方法 ，在這類方法中，他們普遍會放一個hash-based data structure在switch中累計量測，每當有packet進來時 則利用hash flow id的方式更新相對應格子的值， 如此一來既能利用調整memory用量的方式來維持準確度，又不會給系統帶來龐大的overhead
因此目前考量到overhead跟準確度的關係，所以主流的量測常常都是使用sketch based的方法

## Slide 4: Sketch
Two-dimensional array with depth d and width w
Insert
Query
d=4
w=3
[1]G. Cormode and S. Muthukrishnan. An improved data stream summary: The count-min sketch and its applications. Journal of Algorithms, 55(1):58–75, 2005. Conference version in Proceedings of Latin American Theoretical Informatics (LATIN), 2004. Initial Technical Report published as DIMACS 2003-20, June 2003.
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0 | 0 | 0
0+1 | 0 | 0
0 | 0 | 0+1
0 | 0+1 | 0
0+1 | 0 | 0
F1
F2
h1(.)
h2(.)
h3(.)
h4(.)
4 | 52 | 31
5 | 20 | 3
14 | 2 | 9
74 | 3 | 6
h1(.)
h2(.)
h3(.)
h4(.)
Flow ID (or 5-turple)
Packet count of flow (5-turple) = min(4,3,2,74) = 2
Update the hashed bucket of each row

## Slide 5: Sketch-Based Monitoring
Sketch based
  Count-Min(CM) Sketch [1]
  Count Sketch [2]
  Univmon [3]
  ……
Hybrid Sketch Algorithm
  Elastic Sketch [4]
  HybridSketch [5]
  ……
[2]M. Charikar, K. Chen, and M. FarachColton, “Finding frequent items in data streams,” in Proceedings of the International Colloquium on Automata, Languages and Programming, 2002.
[3]Z. Liu, A. Manousis, G. Vorsanger, V. Sekar, and V. Braverman, “One sketch to rule them all: Rethinking network flow monitoring with UnivMon,” in ACM SIGCOMM, 2016.
[4]T. Yang, J. Jiang, P. Liu, Q. Huang, J. Gong, Y. Zhou, R. Miao, X. Li, and S. Uhlig, “Elastic sketch: Adaptive and fast networkwide measurements,” in ACM SIGCOMM, 2018. [5]X. Zhao, M. Wen, M. Tang, Q. Huang, and C. Zhang, “HybridSketch: A memorycentric precise approach for flow measurement,” in IEEE ICC, 2020.

## Slide 6: Sketch-Based Monitoring
Pros
  Memory & Accuracy Tradeoff
  Efficiency
  Generality [Univmon, Sigcomm16]
Notes: 隨著sketch逐漸成為主流量測監控的方法，這類的演算法也越來越多元，雖然他們設計的目的各有所不同，但是他們相較於其他測量方法都有三個共同的優點 首先，
第一點，普遍sketch都具備理論上可以證明的，準確度與記憶體使用量的平衡特性，所以他們可以在只占用少量的空間資源情況下，提供卓越的準確度
其次，因為他們的演算法沒有過多複雜的運算過程，所以即使在高速的網路環境當中，也可以比其他演算法更有效地儲存累計flow 的訊息量
最後，近年來這類的研究，都漸漸追求讓sketch可以更general，使得一套演算法可以同時處理多種的量測項目

## Slide 7: Sketch-Based Monitoring
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 2 | 0 | 0 | 0
Cons
  Collision
  Overloaded per switch
F1
F2

## Slide 8: Sketch-Based Monitoring

## Slide 9: Per-Switch Monitoring
F1
F2
F3
F4
 Each switch is overloaded
 Many switches experience collisions

## Slide 10: Cooperative Monitoring
F1
F2
F3
F4
 Offload monitoring load across switches
 Lower collision probability per switch

## Slide 11: Goal
Alleviate the degree of collisions
Reduce the Relative Error(RE) of all flows
Enhance efficiency of packet processing
Multi-Switch Cooperative Monitoring

## Slide 12: Challenges
How to assign flows to switches?
  Distribute monitoring load across switches
  Jointly consider routing to enhance offloading opportunities
How to provide heterogeneous monitoring resolutions for different flows?
  More important flows, higher monitoring precision
Notes: 要設計一個合作式平台需要解決兩個問題
首先我們要先決定如何幫每個flow選定適當的switch(來追蹤流量)，確保每個flow都能被適當的追蹤
另外我們也需要綜合考慮flow的路由機制，讓所有switch能有更多的機會去平攤追蹤的負擔
另外因為每個flow的大小和重要性不同，我們也需要探討如何提供不同flow異質化的追蹤可靠度。理想上，我們希望越重要的flow能夠獲得更多switch的資源來達到較高的追蹤準確度

## Slide 13: Outline
Overview
Design
Performance Evaluation
Conclusion

## Slide 14: Problem Statement
Input
  A set of switches and a set of flows
Task
  Determine the routing path of flows
  Determine the monitoring switches of each flow
Objective
  Minimize the WRE(Worst Relative Error) of all flows

## Slide 15: Flow Chart
Flow selection
Path selection
Switch selection
Choose the worst Flow
Compute the RE of flow
Can its RE be lowered?
Yes
No
End
Choose the best path

## Slide 16
Flow selection
Path Selection
Switch Selection
Can its RE be lowered?

## Slide 17: Questions
1. How to calculate multi-switch RE of flow f ?
2. How to find the best switch along k-shortest path ?
3. How to query across cooperative switches ?

## Slide 18: Calculate Multi-Switch RE of Flow f
Relative Error(RE)
How to evaluate the performance of cross-switch RE of a flow?

## Slide 19: Cross-Switch RE of a Flow
How to evaluate the performance of cross-switch RE of a flow?
4 | 52 | 31
5 | 20 | 3
14 | 2 | 9
74 | 3 | 6
192.168.1.1
45 | 23 | 14
55 | 80 | 43
18 | 29 | 37
74 | 5 | 18
h1(.)
h2(.)
h3(.)
h4(.)
h1(.)
h2(.)
h3(.)
h4(.)
RE = min{4,5} = 4

## Slide 20: Path Selection
Potential Routing Algorithms
  Shortest path
  Longest path
  K-shortest path

## Slide 21: Path Selection
Naïve way: Shortest Path
  Every flow uses the same path
S1
S2
S3
Set of switch
={s1,s2,s3}
S4
S5
S6
S7
Set of switch
={s1,s2,s3}
Set of switch
={s1,s2,s3}
  Switch congestion  monitoring errors

## Slide 22: Path Selection
Naïve way: Longest Path
  Go through too many switches
  More offloading opportunities  Bandwidth waste

## Slide 23: Path Selection
K-Shortest path
  Yen's Algorithm[6]
  Use path loading and switch to choose best path
S1
S2
S3
S4
S5
S6
S7
First Path
={s1,s2,s3}
Set of best k-path
={[s1,s2,s3]}
[6] Jin Y. Yen “FINDING THE K SHORTEST LOOPLESS PATHS IN A NETWORK*, 2009.

## Slide 24: K-Shortest path
S1
S2
S3
S4
S5
S6
S7
First Path
={s1,s2,s3}
Set of best k-path
={[s1,s2,s3]}
Turn 1
={}

## Slide 25: K-Shortest path
Turn 1
={}
S1
S2
S3
S4
S5
S6
S7
First Path
={s1,s2,s3}
Set of best k-path
={[s1,s2,s3]}
Turn 1
={[s1,s6,s7,s3]}

## Slide 26: K-Shortest path
S1
S2
S3
S4
S5
S6
S7
First Path
={s1,s2,s3}
Set of best k-path
={[s1,s2,s3]}
Turn 1
={[s1,s6,s7,s3]}

## Slide 27: K-Shortest path
S1
S2
S3
S4
S5
S6
S7
second Path
={s1,s6,s7,s3}
Set of best k-path
={[s1,s2,s3],
[s1,s6,s7,s3]}
Turn 2
={ }

## Slide 28: K-Shortest path
S1
S2
S3
S4
S5
S6
S7
second Path
={s1,s6,s7,s3}
Set of best k-path
={[s1,s2,s3],
[s1,s6,s7,s3]}
Turn 2
={ }

## Slide 29: K-Shortest path
S1
S2
S3
S4
S5
S6
S7
second Path
={s1,s6,s7,s3}
Set of best k-path
={[s1,s2,s3],
[s1,s6,s7,s3]}
Turn 2
={ }

## Slide 30: K-Shortest path
S1
S2
S3
S4
S5
S6
S7
second Path
={s1,s6,s7,s3}
Set of best k-path
={[s1,s2,s3],
[s1,s6,s7,s3]}
Turn 2
={ }

## Slide 31: Path Selection
Flow1
Flow2
Flow3
S1
S2
S3
Set of switch
={s1,s2,s3}
S4
S5
S6
S7
Set of switch
={s1,s4,s5,s3}
Set of switch
={s1,s6,s7,s3}

## Slide 32: Query Across Cooperative Switches
4 | 52 | 31
5 | 20 | 3
14 | 2 | 9
74 | 3 | 6
192.168.1.1
45 | 23 | 14
55 | 80 | 43
18 | 29 | 37
74 | 5 | 18

## Slide 33: Multi-Switch Sketch

## Slide 37
Stop when no better switch found

## Slide 39: Outline
Overview
Algorithm
Performance Evaluation
Conclusion

## Slide 40: Comparison Schemes and Metrics
Baseline schemes
  CM sketch
  Best one in the shortest path (Shortest)
  Best one in the network (All)
Performance metrics
  WRE (Worst Relative Error)

## Slide 41: Topology
K-Ary Fat-Tree
  K = 6, K = 4
  K = 4-1 , k = 4-2 , k = 4-3
Notes: 這邊要說為什麼要做出這些topo
為了是要檢查不同雍塞程度的效果

## Slide 42: WRE with Different Topology
Sketch d = 5,w = 3
Multi-Switch Sketch performs well even when resources are limited

## Slide 43: Heterogeneous Monitoring Resolutions
More important flows  higher monitoring precision
a/b a: when a switches are enabled
b: flows using b switches

## Slide 44: Memory Usage
D = 5(95%), w = 3(0.9), w = 6(0.45), w = 9(0.3)
D = 6, w = 9

## Slide 45: Impact of Memory Sizes
Multi-Switch Sketch reduces WRE by up to 97.5%
Notes: 97.5%

## Slide 46: Traffic Distribution
Various distributions of Src and Dst

## Slide 47: Impact of Traffic Distribution
Multi-Switch Sketch leverages multiple switches to alleviate congestion

## Slide 48: Conclusion
Multi-Switch Sketch:
  Alleviate the degrees of collisions by cooperative monitoring
  Improve the WRE of all flows
  Jointly consider routing to enhance offloading opportunities
  Outperform baseline schemes in different scenarios

## Slide 49: Thank you for listening!